Contents

Page

2	Machinery Check – Who and now often?

4-5	Ropes

6	Lifting Equipment

7-8	Working at Height

Fuel Tank Check

High Visability Clothing

Manual Lifting Limits

9-11	Noise

| Country | Machinery check – who and how often? |
| --- | --- |
|  | 1st use | Yearly or > | otherwise | After major modifications |
| Europe | „Conformity“ according Machinery Directive (MD); CE (type approval for „annex IV machines“ Responsible: Manufacturer Check frequency: no special requirements (For EMM, drill and piling rigs → additional requirements for cranes) |
| Austria | CE mark | ABC*, every 4 years AB* A: whit hole, civil engineering, TÜV B: engineering department, elevator keeper C: internal competent person for example asbestos, quartz |  | ABC*, every 4 years AB* |
| Belgium | External organisation (notified body) | External organisation (notified body) | External organisation (three monthly) (notified body) | Same as first use |
| Czech Republic | Conformity according Machinery Directive (MD); Law 387/2001EU by manufacturer | External Organisation or internal „competent person“ once a year |  |  |
| France | External organisation | External Organisation or internal („competent person“) – frequency depending on machinery (usually yearly or twice a year) |  |  |
| Germany | CE mark | Internal („competent person“). Frequency acc. and company internal risk assessment (yearly) |  | Internal („competent person“) (For EMM, drill and piling rigs → additional requirements for cranes) |
| Hungary |  | Only certified supervisor. Min. 5 years. If the manufacturer demands it, then more often. |  |  |
| Spain | External organisation | External organisation: Yearly for machines over 10 years Every 2 years for machines between 6 and 10 years Every 3 years for machines < 6 years (just for cranes) | Internal („competent person“), every 6 months |  |
| Sweden | External organisation (after 36 months) | Extern. org. after 36 + 24 months Extern org. then yearly |  |  |
| Switzerland | CE mark | Internal („competent person“). Frequency is open to company internal risk assessment (usually yearly) _______ For all machines there is a new directive for licences coming 2009/2010. For cranes and forklifts there are additional licences needed. |  | After major modifications or special occurrences by internal organisation (competed person) |
| The Netherlands | External organisation | - |  | After new assembly by external organisation or competed person |

| Country | Ropes |
| --- | --- |
|  | Only deep foundation use (safety factor) | Used for lifting (safety factor) | Top lifting protection | Rope-winch protection |
| Europe | EN 791: 3,00 EN 996: 3,55 | MD: 5,00 | Automatic stop (compulsory) | EN 791 and EN 996: min. 3 revolutions left on the winch |
| Austria | According to relevant EU standards | According to relevant EU standards | According to relevant EU standards | According to relevant EU standards |
| Belgium | 3,55 | 5 | Automatic stop (compulsory) | min. 3 revolutions left on the winch (compulsory) |
| Czech Republic | According to relevant EU standards | According to relevant EU standards | According to relevant EU standards | According to relevant EU standards |
| France | EN 791: 3,00 EN 996: 3,55 | 5 | Automatic stop (compulsory) | min. 3 revolutions left on the winch (compulsory) |
| Germany | According to relevant EU standards | According to relevant EU standards | According to relevant EU standards (compulsory) | According to relevant EU standards |
| Hungary | 6 (to be checked every 6 months) | 6 (to be checked every 6 months) | Compulsory, it has to be checked at the beginning of every work-shift. | Compulsory, it has to be checked at the beginning of every work-shift. |
| Spain | 6 | 6 | Automatic stop (compulsory) | min. 3,5 revolutions left on the winch (compulsory) |
| Sweden | According to relevant EU standards | According to relevant EU standards | According to relevant EU standards | According to relevant EU standards |
| Switzerland | According to national standards as SECURO, EKAS, AZSBV | According to national standards as SECURO, EKAS, AZSBV | According to national standards as SECURO, EKAS, AZSBV (compulsory) | According to national standards as SECURO, EKAS, AZSBV |

| Country | Lifting equipment |
| --- | --- |
|  | Check | Who and frequency | Safety factor |
| Europe | No common rules! | No common rules! | No common rules! |
| Austria | See machinery | See machinery | See machinery |
| Belgium | Certificate (external organisation) | Three monthly (external organisation) | 5 |
| Czech Republic | See machinery | See machinery | See machinery |
| France | Twice a year by external organisation | Control report |  |
| Germany | See machinery (no special requirements) | See machinery (no special requirements) |  |
| Hungary | - | - | - |
| Spain | Certificate (external organisation) | by external organisation |  |
| Sweden | Yearly | by external organisation |  |
| Switzerland | National construction association standard, Verordnung AZSBV | by internal organisation (competent person) |  |

| Country | Working at height | Fuel tank check | High visibility clothing | Manual lifting (maximum) |
| --- | --- | --- | --- | --- |
|  | Limit value | Harness check by | Who? | When? |  |  |
| Europe | No limit value – “risk assessment” | ???? | No common rule! | No common rule! | No common rule! | 25 kg |
| Austria | > 2m 1 m traffic ways, holes in the ground 0 m working besides water | Measures: Fixed guards; safety scaffold; safety harness Competent person (yearly) | No regulations on construction sites, mobile tanks (IBC) based on ADR |  | General: Compulsory (EN 471) - tunnelling - along roads - along railways | The discussion about that issue is going on |
| Belgium | > 2 m | Measure: Fall protection External org. (yearly) | External org. | Every 3 years | General: advised not compulsory Along roads: compulsory (orange/yellow) Along railways: compulsory (only yellow) | 25 kg |
| Czech Rep. | > 2 m | Measure: Fall protection Internal competent pers. (yearly) | External org. | yearly | General: advised not compulsory Along roads: compulsory (green) Along railways: compulsory (spec. requirements) | 55 kg for men 25 kg for woman |
| France | No limit value since 2004 | External org. or comp. pers. (yearly) | External org. | ?? | General: advised not compulsory Along roads: compulsory (orange or yellow – class 2) Along railways: special requirements | 55 kg (medical check) |
| Germany | > 2 m | Measures: Fixed guards; safety scaffold; safety harness Manufacturers’ adv. & internal risk assessment (yearly) | External org. | Every 5 years | General: advised not compulsory Along roads: compulsory (orange) Along railways: special requirements | 25 kg |
| Hungary | > 2 m guard railing, and personal pro-tection (safety belt) | Measures: Fixed guards; safety harness Local manager | At the petrol station | - | Compulsory if there are mobile machinery on the site | For men 50 kg For women 25 kg For young people: 15-20 kg |
| Spain | > 2 m | Measure: Fall protection Internal/external organisation (before use and yearly ) | External org. | Every 10 years | General: advised not compulsory Along roads: compulsory (orange or yellow Along railways: compulsory (only yellow) | 35 kg for eventual works 25 kg for continuous works |
| Sweden | > 2 m | Measures: Fixed guards; safety scaffold; safety harness Internal (yearly) | External org. | Every 3-12 years depending on type | General: all working sites affected by any traffic – compulsory according to EN 471 | 25 kg |
| Switzerland | According to national standards as SECURO, EKAS, AZSBV | According to national standards as SECURO, EKAS, AZSBV | External org. | Every 5 years | General: advised not compulsory Along roads: compulsory (orange) Along railways: special requirements | 25 kg |

| Country | Noise | Operator |
| --- | --- | --- |
|  | Lower action value | Upper action value | Limit value | Training | Medical check |
| Europe | 80 dB(A) | 85 dB(A) | 87 dB(A) | No common rules! | No common rules! |
| Austria | 80 dB(A) PPE advised Instruction Medical check advised | 85 dB(A) PPE compulsory Instruction Action to reduce noise Signing medical check |  | Employers’ responsibility; working/travelling in public traffic zones Minimal training: “Training” driving licence (sufficient) Optional: Many courses “on the market” but no legal requirements, internal trainings |  |
| Belgium | 80 dB(A) PPE advised Instruction Medical check advised | 85 dB(A) PPE compulsory Instruction Action to reduce noise Signing medical check | 87 dB(A) Direct action Identification of the cause Preventive action to avoid repetition | Minimal training: within company Optional: ODF-MOD II | Compulsory (yearly) |
| Czech Republic | 80 dB(A) PPE advised Instruction Medical check advised | 85 dB(A) PPE compulsory Instruction Action to reduce noise Signing medical check | 87 dB(A) Direct action Identification of the cause Preventive action to avoid repetition | Minimal training: within the company (optional) | Compulsory (yearly) |
| France | 80 dB(A) PPE advised Instruction | 85 dB(A) PPE compulsory Action to reduce noise | 87 dB(A) Limit value with PPE | ? | Compulsory (once every two years or yearly or every 6 months (depending on the type of work or risk encountered) |
| Germany | 80 dB(A) PPE advised Instruction Medical check advised | 85 dB(A) PPE compulsory Instruction Action to reduce noise Signing medical check | ?? dB(A) | Employers’ responsibility; working/travelling in public traffic zones Minimal training: “Training” driving licence (sufficient) Optional: Many courses “on the market” but no legal requirements, internal trainings | Not compulsory (but for special professions/trades) Must be offered to the employees |
| Hungary |  |  | > 85 dB(A) PPE compulsory | Driver licence is compulsory. For big machinery with medical check; for simple equipment driving licence is sufficient. | Before employment medical check is compulsory, afterwards yearly |
| Spain | 80 dB(A) PPE advised Instruction Medical check advised | 85 dB(A) PPE compulsory Instruction Action to reduce noise Signing medical check | 87 dB(A) Direct action Identification of the cause Preventive action to avoid repetition | Minimal training: within the company | Compulsory (yearly) |
| Sweden | According to relevant EU Standards (or see Germany) | According to relevant EU Standards (or see Germany) | According to relevant EU Standards (or see Germany) | Minimal training: site and rig operators 6 days theory; 5400 total practical training hours of which 3600 in foundation. For rig operators 1200 of 3600 hours in rig | Compulsory risk assessment and according to physical agent directive (vibration and noise) |
| Switzerland | 80 dB(A) Decree of noise of the Swiss government and cities Instruction Medical check by SUVA | 90 dB(A) PPE compulsory Instruction Action to reduce noise Medical check by SUVA | 95 dB(A) Direct action Identification of the cause Monetary fine | Employers’ responsibility; working/travelling in public traffic zones Minimal training: “Training” driving licence (sufficient) Optional: Many courses “on the market” but no legal requirements, internal trainings | Not compulsory (but for special professions/trades) |